## Slide 1: VRRP Principles and Configurations

## Slide 2
User terminals on a LAN often access the external network through the configured default gateway. If the default gateway fails, network access of all the user terminals is terminated. Consequently, there will be huge loss. You can deploy multiple gateways to solve single-point failures. How do these gateways work collaboratively without conflicts?
VRRP is used to solve the preceding problem. It can implement gateway backup and prevent conflicts of multiple gateways. How is VRRP implemented? How is VRRP configured?

## Slide 3
Upon completion of this section, you will be able to:
  Master VRRP principles
  Understand the VRRP active/standby switchover
  Master VRRP configurations

## Slide 4
VRRP Background and Overview
VRRP Active/Standby Switchover
VRRP Load Balancing
Basic VRRP Configuration

## Slide 5: Limitations of a Single Gateway
When RouterA fails, the devices that use RouterA as the gateway cannot communicate with the Internet.
RouterA

## Slide 6: Problems of Multiple Gateways
  Multiple gateways can be deployed to implement gateway backup.
  However, many problems may occur. IP addresses of gateways conflict, and hosts frequently use different egresses.
192.168.1.254
192.168.1.254

## Slide 7: VRRP Overview
  VRRP virtualizes multiple routers into a virtual router without changing the networking and uses the IP address of the virtual router as the default gateway IP address, implementing gateway backup.
  Protocol versions: VRRPv2 (commonly used) and VRRPv3
  VRRPv2 applies only to IPv4 networks, whereas VRRPv3 applies to both IPv4 and IPv6 networks.
  VRRP packets
  Advertisement packets: The destination IP address is 224.0.0.18, the destination MAC address is 01-00-5e-00-00-12, and the protocol number is 112.

## Slide 8: Basic VRRP Architecture
HostA
Gateway address: 10.1.1.254
IP address: 10.1.1.3/24
Eth0/0/0: 10.1.1.1
RouterA
Master
Priority 150
RouterB
Backup
Priority 100
HostA
Gateway address: 10.1.1.254
IP address: 10.1.1.3/24
Virtual router
vrrp vrid1
Virtual IP address: 10.1.1.254/24
Virtual MAC address: 0000-5e00-0101
Eth0/0/0: 10.1.1.2
Notes: Basic concepts of VRRP:
  VRRP router: device running VRRP. For example, RouterA and RouterB are VRRP routers.
  Virtual router: VRRP group consisting of one master and multiple backups. The VRRP group's virtual IP address is used as the default gateway address on a LAN. For example, RouterA and RouterB form a virtual router.
  Virtual router master: VRRP device that forwards packets. RouterA is the virtual router master.
  Virtual router backup: a group of VRRP devices that do not forward packets. When the master is faulty, a backup with the highest priority becomes the master. RouterB is the virtual router backup.
  Priority: priority of a device in a VRRP group. The value ranges from 0 to 255.The value 0 indicates that a device does not join a VRRP group and is used to enable the backup to immediately become the master without waiting for the timeout. The value 255 is reserved for the IP address owner and cannot be manually configured. The default value is 100.
  VRID: virtual router ID. The VRID of the virtual router composed of RouterA and RouterB is 1. The value is manually configured and ranges from 1 to 255.
  Virtual IP address: IP address of a virtual router. A virtual router can be assigned one or more virtual IP addresses. Virtual IP addresses are configurable. The virtual IP address of the virtual router composed of RouterA and RouterB is 10.1.1.254/24.
  IP address owner: VRRP device that uses an IP address of a virtual router as the actual interface address. If an IP address owner is available, it always functions as the virtual router master.
  Virtual MAC address: MAC address that is generated by the virtual router based on the VRID. A virtual router has one virtual MAC address and is in the format of 00-00-5E-00-01-{vrid}.The virtual router sends ARP Reply packets carrying the virtual MAC address but not the interface MAC address. The VRID of the virtual router composed of RouterA and RouterB is 1, so the MAC address of the VRRP group is 00-00-5E-00-01-01.

## Slide 9: State Machine
Initialize
Master
Backup
Startup & priority=255
Startup & priority!=255
Shutdown
Shutdown
Master_Down_Interval expire | Priority=0 in received packet | Priority in received packet <Own Priority
Priority in received packet >Own Priority
Notes: VRRP defines three statuses: Initialize, Master, and Backup.
The conditions for state transition are as follows:
  Initialize->Master: Startup priority=255
  Initialize->Backup: Startup priority！=255
  Master->Initialize: The device is powered off.
  Master->Backup: The device receives packets with a higher priority than its priority.
  Backup->Initialize: The device is powered off.
  Backup->Master: The device does not receive VRRP Advertisement packets within the timeout interval; the priority of the master in the received Advertisement packet is 0; the priority of the master in the received Advertisement packet is lower than its own priority.

## Slide 10
VRRP Background and Overview
VRRP Active/Standby Switchover
VRRP Load Balancing
Basic VRRP Configuration

## Slide 11: Working Process of VRRP Active/Standby Switchover
HostA
Gateway address: 10.1.1.254
IP address: 10.1.1.3/24
RouterA
RouterB
VRRP
priority 100
ip address 10.1.1.2 virtual ip 10.1.1.254
Master
Backup
VRRP
priority 150
ip address 10.1.1.1 virtual ip 10.1.1.254
1. Select the master.
  2. Maintain the status.
  The master periodically sends VRRP Advertisement packets to other devices in the group to notify that it works properly.
Notes: The VRRP working process is as follows:
  Selecting the master
    VRRP determines the master based on device priorities. The master sends gratuitous ARP packets to notify the connected network devices or hosts of the virtual MAC address of the VRRP group, and forwards packets.
    Election rule: The device with the highest priority becomes the master. When two devices have the same priority and the master already exists, the master retains its status. If there is no master, the IP addresses are compared. The device with a larger interface IP address becomes the master.
  Advertising the master status (maintaining the VRRP group status)
    The master periodically sends VRRP Advertisement packets to advertise its configuration (for example, priority) and running status. The backup determines whether the master works properly based on the received VRRP packets. When the master abandons its role (for example, the master is deleted from the VRRP group), it sends Advertisement packets with the priority of 0. In this case, the backup can rapidly switch to be the master, without waiting for Master_Down_Interval timer. This switching time is called Skew_Time and is calculated as follows:
    Skew_Time = (256 – Priority of the backup)/256
    The unit is second.
    When the master fails and cannot send VRRP Advertisement packets, the backup cannot immediately lean the working status of the master. After Master_Down_Interval expires, the backup considers that the master fails and switches to be the master.
    Master_Down_Interval = 3 x Advertisement_Interval + Skew_time
    The unit is second.

## Slide 12: VRRP Active/Standby Switchover (1/2)
If the master fails, the active/standby switchover is as follows.
RouterA
RouterB
Backup
Master
Master
VRRP
priority 150, ip add1.1.1.1
VRRP
priority 100, ip add1.1.1.2
When the backup does not receive Advertisement packets from the master within Master_Down_Interval, it immediately becomes the master.
Notes: The process is as follows when the master fails:
  If the backup does not receive Advertisement packets after the timer (Master_Down_Interval) expires, the backup becomes the master. The calculation formula is as follows:
  Master_Down_Interval = 3 x Advertisement_Interval + Skew_time
  When there are multiple backups in a VRRP group, multiple master devices may occur in a short period of time. In this case, the device compares the priority in the received VRRP packets with the local priority and the device with the highest priority becomes the master.
  After the device becomes the master, it immediately sends gratuitous ARP packets to update MAC address entries so that user traffic is diverted to itself. The process is transparent for users.

## Slide 13: VRRP Active/Standby Switchover (2/2)
When the original master fails, the revertive switching is as follows:
RouterA
RouterB
Master
VRRP
priority 100, ip add1.1.1.2
Backup
Master
VRRP
priority 150, ip add1.1.1.1
When RouterA finds that the priority in packets received from RouterB is lower than RouterA, RouterA immediately preempts to be the master.
Which problem may occur when the master is preempted immediately?
Notes: Preemption mode:
  If the priority of a virtual router backup is higher than the priority of the current virtual router master, the virtual router backup automatically becomes the virtual router master. By default, a device works in preemption mode.
  If the IP address owner is available, it always works in preemption mode and becomes the master.
Preemption delay:
  By default, the preemption delay is 0 seconds, indicating immediate preemption.
  If RouterA immediately preempts to be the master after recovery, traffic may be interrupted. This is because convergence of a routing protocol on the uplink of RouterA is not completed. In this case, the preemption delay needs to be configured.
  on an unstable network, the backup may not receive packets from the master within Master_Down_Interval due to congestion. The backup switches to be the master. When packets from the original master reach the new master, the new master switches to be the backup. Consequently, members of the VRRP group frequently switch their statuses. To resolve this issue, you can configure the preemption delay so that the backup waits for Master_Down_Interval and preemption delay. If the backup does not receive VRRP Advertisement packets during this period, the backup switches to be the master.

## Slide 14: VRRP Fault
RouterA
RouterB
Master
Backup
Question: Which failure point may cause a VRRP active/standby switchover?
HostA
Notes:     The uplink fault on RouterA does not trigger a VRRP active/standby switchover. As a result, HostA's Internet access traffic is discarded at the RouterA. VRRP needs to detect the uplink fault and a VRRP active/standby switchover can be performed in a timely manner.
    When RouterA or the interface of RouterA connected to RouterB fails, a VRRP active/standby switchover is triggered. This is because the backup cannot receive protocol packets sent by the master within Master_Down_Interval.

## Slide 15: VRRP Association
Solution: VRRP association can be configured to monitor the uplink interface or link fault and perform an active/standby switchover.
RouterA
Route rB
Backup
Master
The uplink is Down, but the master and backup exchange packets normally and no switching is performed. Consequently, host access is abnormal.
VRRP
Notes: Problem: VRRP cannot detect the status change of the interface that is not enabled with VRRP. When the uplink fails, VRRP cannot detect the fault and an active/standby switchover is not performed, causing service interruption.
Solution: VRRP association can be configured to monitor the uplink interface or link fault and perform an active/standby switchover.

## Slide 16
VRRP Background and Overview
VRRP Active/Standby Switchover
VRRP Load Balancing
Basic VRRP Configuration

## Slide 17: VRRP Load Balancing Working Process
RouterA
Gateway:10.1.1.10
IP address:10.1.1.3/24
Gateway:10.1.1.10
IP address:10.1.1.4/24
Gateway:10.1.1.11
IP address:10.1.1.5/24
RouterB
vrid1
virtual ip :10.0.0.10
Backup
vrid2
virtual ip :10.0.0.11
Master
vrid1
virtual ip :10.0.0.10
Master
vrid2
virtual ip :10.0.0.11
Backup
Traditionally, all traffic is forwarded by the master in active/standby mode. The master is overloaded.
You can configure different VRRP groups so that RouterB becomes the master of the new VRRP group to load balance traffic.
HostA
HostB
HostC
Master
Backup
It is idle.
Notes: In load balancing mode, multiple VRRP groups forward service traffic. The principles and negotiation process of the VRRP load balancing mode and VRRP active/standby mode are the same. Each VRRP group consists of one master and multiple backups.
Unlike the active/standby mode, the load balancing mode requires establishment of multiple VRRP groups. Different devices are used as masters for the VRRP group. A device can play different roles in multiple VRRP groups.

## Slide 18
VRRP Background and Overview
VRRP Active/Standby Switchover
VRRP Load Balancing
Basic VRRP Configuration

## Slide 19: VRRP Configuration
RouterA
vrid1 virtual ip :10.0.0.10
Master
vrid2 virtual ip :10.0.0.11
Backup
RouterB
vrid1 virtual ip :10.0.0.10
Backup
vrid2 virtual ip :10.0.0.11
Master
G0/0/1
ip address:10.0.0.2
G0/0/1
ip address:10.0.0.1
RouterC
G0/0/0
G0/0/0
G0/0/1
ip address:10.0.0.1
G0/0/1
ip address:10.0.0.2
RouterC
G0/0/0
G0/0/0
Configure RouterB.
interface GigabitEthernet0/0/1
ip address 10.0.0.2 255.255.255.0
vrrp vrid 1 virtual-ip 10.0.0.10
Configure RouterA.
interface GigabitEthernet0/0/1
ip address 10.0.0.1 255.255.255.0
vrrp vrid 1 virtual-ip 10.0.0.10
vrrp vrid 1 priority 120
vrrp vrid 1 preempt-mode timer delay 20
vrrp vrid 1 track interface GigabitEthernet0/0/0 reduce 30
vrrp vrid 2 virtual-ip 10.0.0.11
Configure RouterB. interface GigabitEthernet0/0/1
ip address 10.0.0.2 255.255.255.0
vrrp vrid 1 virtual-ip 10.0.0.10
vrrp vrid 2 virtual-ip 10.0.0.11
vrrp vrid 2 priority 120
vrrp vrid 2 preempt-mode timer delay 20
vrrp vrid 2 track interface GigabitEthernet0/0/0 reduce 30
HostA
HostB
HostC
RouterA
vrid1 virtual ip :10.0.0.10
Master
RouterB
vrid1 virtual ip :10.0.0.10
Backup
Configure RouterA.
interface GigabitEthernet0/0/1
ip address 10.0.0.1 255.255.255.0
vrrp vrid 1 virtual-ip 10.0.0.10
vrrp vrid 1 priority 120
vrrp vrid 1 preempt-mode timer delay 20
vrrp vrid 1 track interface GigabitEthernet0/0/0 reduce 30
Active/Standby mode
Load balancing mode
Notes: The configuration roadmap in load balancing mode is similar to that in active/standby mode. A VRRP group is used as an example. The configuration of the master is as follows:
  vrrp vrid 1 virtual-ip 10.0.0.10 //Configure the virtual IP address of VRRP group 1.
  vrrp vrid 1 priority 120 //Set the device priority in VRRP group 1 to 120. The priorities of other devices are not specified manually, so the default value of 100 is used. The local device is the master.
  vrrp vrid 1 preempt-mode timer delay 20 //Set the preemption delay of the master to 20s.
  vrrp vrid 1 track interface GigabitEthernet0/0/0 reduce 30 //Associate VRRP with the uplink interface G0/0/0. When G0/0/0 fails, the VRRP priority of the master is reduced by 30.
Configuration of the backup:
  vrrp vrid 1 virtual-ip 10.0.0.10 //Configure the virtual IP address of VRRP group 1.

## Slide 20
Which of the following statements about the VRRP master is false?
  The VRRP master periodically sends VRRP packets.
  The VRRP master uses the virtual MAC address to respond to ARP Request packets carrying the virtual IP address.
  The VRRP master forwards IP packets destined for the virtual MAC address.
  Even if the master already exists, the backup with a higher priority will preempt to be the master.
Notes: Answer: D.