## Slide 1: Route Control

## Slide 2
Enterprise networks may encounter the problems such as unauthorized access of certain traffic and sub-optimal traffic path selection. To ensure data access security and improve link bandwidth usage, traffic behavior on the network must be controlled, for example, reachability control and traffic path adjustment.
Tools may be required to meet complicated and precise traffic control requirements. This course introduces the traffic control tools and their usage scenarios.

## Slide 3
Upon completion of this section, you will be able to:
  Master the method to control network traffic reachability
  Master the method to adjust network traffic paths
  Be familiar with the problems caused by route import and solutions

## Slide 4
Traffic Behavior Control Requirement
Control Reachability
Adjust Network Traffic Path
Problems Caused by Route Importing and Solutions

## Slide 5
Traffic Behavior Control Requirement
Control traffic reachability.
Adjust network traffic path.
Financial department
Headquarters
R&D department
Documentation department
OSPF
Marketing department
To enhance network security, some departments are not allowed to access each other.
In network optimization stage, network traffic paths may need to be adjusted.
Financial department
Headquarters
OSPF
Marketing department
Idle link
10M
10M
10M
5M
Notes: Control traffic reachability: As shown in the figure, the marketing department is not allowed to access the financial and R&D departments, and the headquarters is not allowed to access the R&D department.
Adjust network traffic paths: As shown in the figure, OSPF is run to compute routes. The marketing and financial departments access the headquarters through the path with the minimum cost, even though the path is congested. The other link is always idle, causing a waste of bandwidth.

## Slide 6
Traffic Behavior Control Requirement
Control Reachability
  Routing Policy
  Traffic Filter
Adjust Network Traffic Path
Problems Caused by Route Importing and Solutions

## Slide 7
Question: How to control network traffic reachability.
Control Traffic Reachability
Solution 1: Change the number of routing entries (filter the received and advertised routes) to control reachability. This is called routing policy.
Solution 2: Deploy traffic filter to deny or permit specified traffic flow. This method is called traffic filter.
Financial department
Headquarters
R&D department
Documentation department
OSPF
Marketing department
RTD
RTC
RTB
RTA
Notes: When advertising, receiving, and importing routes, routing policy implements certain policies according to actual networking requirements in order to filter the routes and change the attributes of the routes. Purposes of routing policies are as follows:
  Control route advertisement: advertises only the routes matching certain conditions.
  Control route sending and receiving: receives only necessary and valid routes to control the capacity of routing table, enhancing network security.
  Filter and control imported routes: imports only the routes meeting certain conditions from other routing protocols, and sets the attributes of imported routes.
  Set route attributes: sets attributes for the routes filtered by routing policy.

## Slide 8
Solution 1: Routing Policy
Use the Filter-Policy tool to filter the routes imported from RTA to OSPF and the routes imported from RTC to the routing table:
  Use ACL or IP-Prefix List to match the target flow.
  Use the Filter-Policy in the protocol view to advertise policies for the target flow.
Use the Route-Policy tool to filter the direct routes imported by RTA:
  Use ACL or IP-Prefix List to match the target flow.
  Use the Route-Policy in the protocol view to control the imported routes.
Financial department
Headquarters
R&D department
Documentation department
OSPF
Marketing department
RTD
RTC
RTB
RTA
Notes: Routing policies are implemented in the following steps:
  Define attributes of routing information to which routing policies are applied. Define a set of matching rules regarding various attributes of routing information such as the destination address and AS number.
  Apply matching rules to route advertising, receiving, and importing.
Currently, the following filters are provided for routing protocols:
  ACL
  Address prefix list
  AS_Path filter
  Community attribute filter
  Extended community attribute filter
  RD filter

## Slide 9
ACL classifies packets into different types by based on packet information.
ACL Application Example (1)
acl 2001
rule 0 permit source 1.1.0.0 0.0.255.255
1.1.1.1/32
1.1.1.0/24
1.1.0.0/16
1.0.0.0/8
1.1.1.1/32
1.1.1.0/24
1.1.0.0/16
Notes: An ACL is composed of a list of rules. Each rule contains a permit or deny clause. These rules define packets with information in the packets.
ACL classification:
  Basic ACL: matches packets against source address, fragmentation flag, and time range. The ACL number ranges from 2000 to 2999.
  Advanced ACL: matches packets against source address, destination address, source port number, destination port number, protocol type, priority, and time range. the ACL number ranges from 3000 to 3999.
  Layer 2 ACL: matches packets against source MAC address, destination MAC address, and packet type. The ACL number ranges from 4000 to 4999.
  User-defined ACL: matches packets against user-defined rules. The ACL number ranges from 5000 to 5999.
An ACL can consist of multiple deny or permit clauses. Each clause describes a rule. After receiving data packets, the device matches the packets against the first ACL rule. If the packets do not match the first ACL rule, the device matches the packets against the next ACL rule. Once the packets match a rule, the device executes the action in the rule and does not match packets against other rules. If the packets do not match any rule, the device directly forwards the packets.

## Slide 10
Notes: Note: The ACL rules may overlap or conflict with each other. The rule matching order decides the rule priorities. The ACL processes rule overlapping or conflict based on rule priorities.

## Slide 11
ACL Application Example (2)
acl 2001
rule 0 permit source 1.1.1.1 0
rule 1 deny source 1.1.1.0 0
rule 2 permit source 1.1.0.0 0.0.255.0
rule 3 deny source any
1.1.1.1/32
1.1.1.0/24
1.1.0.0/16
1.0.0.0/8
1.1.1.1/32
1.1.0.0/16

## Slide 12
ACL Application Example (3)
acl 2001
rule 0 permit source 1.1.1.0 0
1.1.1.1/32
1.1.1.0/24
1.1.1.0/25
1.1.0.0/16
1.0.0.0/8
1.1.1.0/24
1.1.1.0/25
Question: How to filter out the route 1.1.1.0/25?
ACL can flexibly match packets against IP address prefixes, but cannot match mask length.

## Slide 13
IP-Prefix List can match both IP address prefix and mask length.
IP-Prefix List cannot filter IP packets, but can filter only routing information.
IP-Prefix List Application Example (1)
ip ip-prefix test index 10 permit 10.0.0.0 16 greater-equal 24 less-equal 28
IP address range: 10.0.0.0 – 10.0.x.x
24<= Mask length<=28
Example: 10.0.1.0/24, 10.0.2.0/25, 10.0.2.192/26
Notes: IP prefix list is the address prefix list. The address prefix list filters the routes based on the defined prefix filter list.
Format and matching rule of prefix list:
  The prefix filter list consists of IP addresses and masks. An IP address can be a subnet address or host address. The mask length ranges from 0 to 32.
  Each IP prefix in the IP prefix list has an index. The IP prefixes are processed in an ascending order of index.
  If the indexes are not manually set, the device allocates indexes to the IP prefixes with an interval of 10. If a new IP prefix has the same name and index as an existing IP prefix but their contents are different, the new IP prefix overwrites the old one.
  If no IP prefix is matched, the default matching mode of the last IP prefix is deny by default. If a referenced IP prefix list does not exist, the default mode permit is used.

## Slide 14
Notes: Prefix mask length range:
The IP prefix list can match a specific route or match the routes within a certain mask length. The prefix mask length can also be specified using the keywords greater-equal or less-equal. If the keyword greater-equal or less-equal is not specified, the precise matching is used. That is, only the route with the same mask length as the prefix list is matched. If the keyword greater-equal is specified, the routes of which the mask lengths range from greater-equal value to 32 bits are matched. If the keyword less-equal is specified, the routes of which the mask lengths range from the specified value to less-equal are matched.

## Slide 15
IP-Prefix List Application Example (2)
ip ip-prefix Pref1 index 10 permit 1.1.1.0 24
greater-equal 24 less-equal 24
1.1.1.1/32
1.1.1.0/24
1.1.1.0/25
1.1.0.0/16
1.0.0.0/8
1.1.1.0/24
The route 1.1.1.0/25 will be filtered out.
"greater-equal 24 less-equal 24" indicates that the mask length is 24.

## Slide 16
Filter-Policy can filter the received or advertised ISIS, OSPF, and BGP routes.
Filter-Policy Tool
Filter the routes received by protocols:
filter-policy { acl-number | ip-prefix ip-prefix-name } import
Filter the routes advertised by protocols:
filter-policy { acl-number | ip-prefix ip-prefix-name } export
Notes: The filter-policy tools of protocols can reference ACLs or address prefix lists to filter the received, advertised, and imported routes.
For a distance-vector protocol and a link-state protocol, the operations of the filter-policy tools are different:
  The distance-vector protocol generates routes based on routing table, so the filter will affect the routes received from and sent to neighbors.
  The link-state protocol generates routes based on the link state base and the routing information is hidden in the link status LSA. However, the filter-policy cannot filter the advertised and received LSAs. Therefore, the filter-policy does not affect link state advertisement, integrity of link state, or routing table. It affects only the local routing table. Only filtered routes can be added to the routing table.
  The routes advertised by the filter-policy export command of different protocols are different:
    The routes imported to or discovered by the DV protocol are filtered.
    Only the routes imported to the link status protocol are filtered.

## Slide 17
Route-Policy Tool
Route-policy is a powerful tool. It can be used together with other tools such as ACL, IP prefix list, and AS path filter.
A route policy consists of multiple nodes, which have the OR relationship. Each node has multiple if-match and apply clauses, and the if-match clauses have the AND relationship.
Format of route policy:
route-policy route-policy-name { permit | deny } node node
  if-match {acl/cost/interface/ip next-hop/ip-prefix}
  apply {cost/ip-address next-hop/tag}
Notes: Each node in the route policy matches permit or deny mode. If a node matches the permit mode, when a route meets all if-match clauses in the node, the route is allowed and the apply clause matching the node is executed, and the next node is not processed. If a route does not match any if-match clause in the node, the next node is processed for route filtering. If a node matches the deny mode, when a route matches all if-match clauses in the node, the route is not allowed and the apply clause of the node is not executed, and the next node is not processed. Otherwise, the next node is processed for route filtering.

## Slide 18
Route-Policy Application Example
Network Cost NextHop
1.1.2.0/24 4687 34.34.34.2
4687 13.13.13.1
1.1.3.0/24 4687 34.34.34.2
4687 13.13.13.1
1.1.3.0/25 1 34.34.34.2
1 13.13.13.1
5.5.5.5/32 4687 34.34.34.2
4687 13.13.13.1
6.6.6.6/32 4687 34.34.34.2
4687 13.13.13.1
Network Cost NextHop
1.1.3.0/24 4687 34.34.34.2
21 13.13.13.1
1.1.3.0/25 11 34.34.34.2
21 13.13.13.1
acl 2001
rule 0 permit source 1.1.3.0 0.0.0.255
acl 2002
rule 0 permit source 13.13.13.1 0
route-policy RP deny node 10
if-match ip-prefix Pref1
route-policy RP permit node 20
if-match ip-prefix Pref2
route-policy RP permit node 30
if-match acl 2001
if-match ip next-hop acl 2002
apply cost 21
route-policy RP permit node 40
if-match ip-prefix Pref3
apply cost 11
route-policy RP permit node 50
#
ip ip-prefix Pref1 index 10 permit 5.5.5.5 32
ip ip-prefix Pref1 index 20 permit 1.1.2.0 24
ip ip-prefix Pref2 index 10 deny 6.6.6.6 32
ip ip-prefix Pref3 index 10 permit 1.1.3.0 24
greater-equal 25 less-equal 25
Table-1
Table-2
Notes: Pref1 matches 5.5.5.5/32 or 1.1.2.0/24. They will be filtered out (deny) by node 10 of route-policy RP, so Table-2 does not contain 5.5.5.5/32 and 1.1.2.0/24.
Pref2 filters out (deny) 6.6.6.6/32. Although node 20 in route-policy RP matches permit, 6.6.6.6/32 is still filtered out. Therefore, Table-2 does not contain 6.6.6.6/32.
Node 30 in route-policy RP defines two if-match clauses, matching ACL 2001 and ACL 2002. The routes match ACL 2001 include 1.1.3.0/24 (next hop 34.34.34.2), 1.1.3.0/24 (next hop 13.13.13.1), 1.1.3.0/25 (next hop 34.34.34.2), and 1.1.3.0/25 (next hop 13.13.13.1). The routes 1.1.3.0/24 (next hop 13.13.13.1) and 1.1.3.0/25 (next hop 13.13.13.1) match both ACL 2001 and ACL 2002. Therefore, the cost values of 1.1.3.0/24 (next hop 13.13.13.1) and 1.1.3.0/25 (next hop 13.13.13.1) are changed to 21.
The routes 1.1.3.0/24 (next hop 34.34.34.2) and 1.1.3.0/25 (next hop 34.34.34.2) are matched against node 40 in route-policy RP. The route 1.1.3.0/25 matches Pref3, so the cost value of 1.1.3.0/25 (next hop 34.34.34.2) is changed to 11.
Then, the route 1.1.3.0/24 (next hop 34.34.34.2) matches node 50 in route-policy RP.

## Slide 19
Route-Policy Configuration (1)
Financial department
Headquarters
R&D department
Documentation department
OSPF
Marketing department
RTD
RTC
RTB
RTA
10.1.4.0
12.1.2.0
12.1.3.0
10.1.5.0
12.1.1.0
10.1.1.0
10.1.2.0
10.1.3.0
ospf 1
area 0
network 12.1.2.0 0.0.0.255
network 10.1.4.0 0.0.0.255
ospf 1
area 0
network 12.1.3.0 0.0.0.255
network 10.1.5.0 0.0.0.255
ospf 1
area 0
network 12.1.1.0 0.0.0.255
network 12.1.2.0 0.0.0.255
network 12.1.3.0 0.0.0.255
ospf 1
import-route direct
area 0
network 12.1.1.0 0.0.0.255

## Slide 20
Route-Policy Configuration (2)
acl 2000
rule 5 deny source 10.1.1.0 0.0.0.255
rule 10 permit source any
ospf 1
filter-policy 2000 import
Financial department
Headquarters
R&D department
Documentation department
OSPF
Marketing department
RTD
RTC
RTB
RTA
10.1.4.0
10.1.5.0
10.1.1.0
10.1.2.0
10.1.3.0
ip ip-prefix ab index 10 permit 10.1.1.0 24
ip ip-prefix ab index 20 permit 10.1.3.0 24
ospf 1
filter-policy ip-prefix ab export direct
Notes: RTA can also use route policy to control routes:
  acl 2000
    rule 0 permit source 10.1.1.0 0.0.0.255
    rule 5 permit source 10.1.3.0 0.0.0.255
  route-policy huawei-control permit node 10
    if-match acl 2000
  ospf 1
    import-route direct route-policy huawei-control

## Slide 21
Route-Policy Configuration (3)
<RTC>dis ip routing-table
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 14 Routes : 14
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.0/24 O_ASE 150 1 D 12.1.2.1 GigabitEthernet 0/0/0
10.1.4.0/24 Direct 0 0 D 10.1.4.2 GigabitEthernet 0/0/1
10.1.5.0/24 OSPF 10 3 D 12.1.2.1 GigabitEthernet 0/0/0
<RTD>dis ip routing-table
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 15 Routes : 15
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.1.0/24 O_ASE 150 1 D 12.1.3.1 GigabitEthernet 0/0/0
10.1.3.0/24 O_ASE 150 1 D 12.1.3.1 GigabitEthernet 0/0/0
10.1.4.0/24 OSPF 10 3 D 12.1.3.1 GigabitEthernet 0/0/0
10.1.5.0/24 Direct 0 0 D 10.1.5.2 GigabitEthernet 0/0/1
Notes: Note: The preceding information is a part of key information.

## Slide 22
Traffic Behavior Control Requirement
Control Reachability
  Routing Policy
  Traffic Filter
Adjust Network Traffic Path
Problems Caused by Route Importing and Solutions

## Slide 23
Based on customized policy: uses the traffic filter.
Solution 2: Traffic Filter(1)
Financial department
Headquarters
R&D department
Documentation department
OSPF
Marketing department
RTD
RTC
RTB
RTA
10.1.4.0
10.1.5.0
10.1.1.0
10.1.2.0
10.1.3.0
acl number 3000
rule 0 deny ip source 10.1.4.0 0.0.0.255 dest 10.1.1.0 0.0.0.255
rule 5 deny ip source 10.1.4.0 0.0.0.255 dest 10.1.2.0 0.0.0.255
rule 10 permit ip source any
int g0/0/1
traffic-filter inbound acl 3000
acl 3000
rule 0 deny ip source 10.1.5.0 0.0.0.255 dest 10.1.2.0 0.0.0.255
int g0/0/1
traffic-filter inbound acl 3000
G0/0/1
G0/0/1

## Slide 24
Solution 2: Traffic Filter (2)
PC-Marketing department>ping 10.1.1.1
Ping 10.1.1.1: 32 data bytes, Press Ctrl_C to break
Request timeout!
Request timeout!
Request timeout!
Request timeout!
--- 10.1.1.1 ping statistics ---
4 packet(s) transmitted
0 packet(s) received
100.00% packet loss
[RTC]dis ip routing-table
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 16 Routes : 16
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.1.0/24 O_ASE 150 1 D 12.1.2.1 GigabitEthernet 0/0/0
10.1.2.0/24 O_ASE 150 1 D 12.1.2.1 GigabitEthernet 0/0/0
10.1.3.0/24 O_ASE 150 1 D 12.1.2.1 GigabitEthernet 0/0/0
10.1.4.0/24 Direct 0 0 D 10.1.4.2 GigabitEthernet 0/0/1
10.1.5.0/24 OSPF 10 3 D 12.1.2.1 GigabitEthernet 0/0/0
Notes: According to the test result, after Traffic Filter is configured, the routing table of RTC contains the routes on the entire network, and the marketing department cannot access the financial and R&D departments but can access other departments. The routing table of RTD also contains the routes on the entire network. The headquarters cannot access the R&D department, but can access other departments.

## Slide 25
Traffic Behavior Control Requirement
Control Reachability
Adjust Network Traffic Path
  Routing Policy
  Policy-based Routing
Problems Caused by Route Importing and Solutions

## Slide 26
In network optimization stage, network traffic paths may need to be adjusted.
Adjust Network Traffic Path - Single Protocol
Solution 1: uses route policy to change the protocol attribute to control routing table entries and adjust traffic path.
Solution 2: uses policy-based routing to control traffic behavior before searching the routing table.
RTC
Financial department
Headquarters
OSPF
Marketing department
Idle link
10M
10M
10M
5M
RTA
RTB
RTD
Notes: You can change protocol attributes to control the routing table entries, affecting traffic path:
  If OSPF or IS-IS is run, adjust the cost values of interfaces.
  If RIP is run, adjust the metric or next hop.
  If BGP is run, adjust the AS-Path, Local_Pref, MED, and Community attributes.

## Slide 27
Solution 1: Routing Policy
Financial department
10 persons
Headquarters
OSPF
Marketing department
20 persons
10M(cost 1)
10M(cost 1)
10M(cost 1)
5M(cost 2)
RTD
RTC
RTB
RTA
12.1.1.0
12.1.2.0
12.1.3.0
12.1.4.0
10.1.1.0
10.1.2.0
10.1.3.0
G0/0/0
int g0/0/0
ospf cost 2
G0/0/1
display ip routing-table
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.0/24 OSPF 10 4 D 12.1.1.2 GigabitEthernet 0/0/0
    OSPF 10 4 D 12.1.3.2 GigabitEthernet 0/0/1
display ip routing-table
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.0/24 OSPF 10 3 D 12.1.1.2 GigabitEthernet 0/0/0
Notes: Traditionally, packets are forwarded by searching the routing table based on destination IP addresses. What are the disadvantages of this method? Can it meet complicated requirements? Can packet forwarding be controlled precisely?

## Slide 28
The traffic path from the marketing department to headquarters is RTA-RTB-RTD, and the traffic path from the financial department to headquarters is RTA-RTC-RTD.
As shown in the figure, solution 1 cannot meet the requirement because packets are forwarded based on destination address. It cannot meet the requirements of source address-based, destination address-based, or application layer-based forwarding
Limitation of Solution 1
RTC
RTB
Financial department
10 persons
Headquarters
OSPF
Marketing department
20 persons
10M
10M
10M
5M
RTD
RTA
Notes: Due to the limitation in route policy, users expect to customize packet forwarding policies based on the traditional routing method. Policy-based routing allows network administrators to make user-defined policies to change packet routes based on source addresses, packet size, and link quality in addition to destination addresses.

## Slide 29
Traffic Behavior Control Requirement
Control Reachability
Adjust Network Traffic Path
  Routing Policy
  Policy-based Routing
Problems Caused by Route Importing and Solutions
Notes: Different from the routing mechanism that forwards packets by searching for the routes based on the destination addresses of IP packets, policy-based routing (PBR) is based on the user-defined routing policies. PBR has a higher priority than routing policy. Before forwarding a data packet, the router matches the packet against the PBR rule first. If matched, the packet is forwarded based on the policy. Otherwise, the packet is forwarded based on the routing table. The PBR does not modify the routing table. It affects data packet forwarding based on the pre-defined rules.

## Slide 30
Solution 2: Policy-based Routing (1)
Policy-based routing is implemented using traffic policy:
  Use ACL to match traffic;
  Define behavior for traffic, for example, change the next hop.
The routing is based on source address. That is, the next hop of traffic from the marketing department is RTB and the next hop of traffic from the financial department is RTC.
RTC
RTB
Financial department
10 persons
Headquarters
OSPF
Marketing department
20 persons
10M
10M
10M
5M
RTD
RTA
G0/0/2
G4/0/0
12.1.1.0
12.1.2.0
12.1.3.0
12.1.4.0
10.1.1.0
10.1.2.0
10.1.3.0
Notes: PBR includes:
  Local PBR: applies to packets sent by the device, such as ICMP and BGP packets.
    To send the packets with different source addresses and lengths, configure local PBR.
    It is implemented using the Policy-Based-Route tool.
  Interface PBR: applies to the packets forwarded (not initiated) by the local device.
    To forward packets to the specified next hop, configure the interface PBR. The packets matching the redirection rule are forwarded through the specified next hop interface. The packets not matching the redirection rule are forwarded based on routing table. Interface PBR applies to load balancing and monitoring.
    It is implemented using the traffic policy.
  Smart PBR: selects the optimal path for service traffic based on link quality.
    To select paths for different services based on link quality, configure smart PBR.
    It is implemented using the Smart-Policy-Route tool. This method is not described in this course.

## Slide 31
Solution 2: Policy-based Routing (2)
[RTA]acl 3001
rule 5 permit ip source 10.1.2.0 0.0.0.255 dest 10.1.3.0 0.0.0.255
traffic classifier huawei-control2
if-match acl 3001
traffic behavior huawei-control2
redirect ip-nexthop 12.1.3.2
traffic policy huawei-control2
classifier huawei-control2 behavior huawei-control2
int g4/0/0
traffic-policy huawei-control2 inbound
[RTA]acl 3000
rule 5 permit ip source 10.1.1.0 0.0.0.255 dest 10.1.3.0 0.0.0.255
traffic classifier huawei-control1
if-match acl 3000
traffic behavior huawei-control1
redirect ip-nexthop 12.1.1.2
traffic policy huawei-control1
classifier huawei-control1 behavior huawei-control1
int g0/0/2
traffic-policy huawei-control1 inbound
Notes: MQC is used in this example.

## Slide 32
Solution 2: Policy-based Routing (3)
PC-Marketing department>tracert 10.1.3.1
traceroute to 10.1.3.1, 8 hops max
(ICMP), press Ctrl+C to stop
1 10.1.1.2 47 ms 31 ms 15 ms
2 12.1.1.2 47 ms 31 ms 32 ms
3 12.1.2.2 93 ms 63 ms 46 ms
4 *10.1.3.1 62 ms 31 ms
PC-Financial department>tracert 10.1.3.1
traceroute to 10.1.3.1, 8 hops max
(ICMP), press Ctrl+C to stop
1 10.1.2.2 16 ms 31 ms 16 ms
2 12.1.3.2 62 ms 47 ms 31 ms
3 12.1.4.2 47 ms 47 ms 31 ms
4 10.1.3.1 32 ms 46 ms 32 ms
<RTA>dis ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------
Routing Tables: Public
Destinations : 19 Routes : 20
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.1.0/24 Direct 0 0 D 10.1.1.2 GigabitEthernet 0/0/2
10.1.2.0/24 Direct 0 0 D 10.1.2.2 GigabitEthernet 4/0/0
10.1.3.0/24 OSPF 10 3 D 12.1.1.2 GigabitEthernet 0/0/0

## Slide 33
Differences Between the Routing Policy and PBR
Routing Policy | Policy-based Routing
Based on the control plane, affect routing entries. | Based on the forwarding plane, do not affect routing entries. Packets are forwarded based on policy first, and then based on routing table if policy-based forwarding fails.
Policy based on destination address. | Policy based on source address, destination address, protocol type, and packet size.
Used with routing protocol. | A routing policy needs to be manually configured hop by hop to ensure that packets are forwarded according to the policy.
Tools: Route-Policy, Filter-Policy, etc. | Tools: Traffic-Filter, Traffic-Policy, Policy-Based-Route, etc.
Notes: A router has a routing table and a forwarding table. The forwarding table is mapped from the routing table. PBR applies to the forwarding table, and routing policy applies to the routing table. Forwarding is performed at the bottom layer, while routing is performed at the upper layer. Therefore, the forwarding based on forwarding table has a higher priority than the forwarding based on routing table.
A route policy takes effect in route discovery. It uses certain rules to influence route advertisement, receiving, and selection, thus modifying the routing entries. The PBR takes effect in packet forwarding. It uses certain rules to influence packet forwarding, but does not affect the routing table.

## Slide 34
Traffic Behavior Control Requirement
Control Reachability
Adjust Network Traffic Path
Problems Caused by Route Importing and Solutions

## Slide 35
In the preceding example, four routers run the same protocol. If they run different protocols, what will happen?
Adjust Network Traffic Path - Multiple Protocols
ospf 1
import-route rip 1 type 1
ospf 1
import-route rip 1 type 1
Financial department
10 persons
Headquarters
Marketing department
20 persons
10M
5M
RTD
RTC
RTB
RTA
10.1.3.0/24 150 3
10.1.3.0/24 150 4
The link is idle. Low link use efficiency.
Solution: Change the OSPF cost on interface to implement load balancing.
RIP
OSPF

## Slide 36
Other Problems Caused by Multi-Protocol - Sub-Optimal Route
Lo0:2.2.2.2
Dest. RIP 100
Dest. RIP 100
import rip
Dest. ISIS 15
Dest. ISIS 15
RTA
RTC
RTB
RTD
S0
12.12.12.1
RIP
ISIS
isis 1
import-route rip 1
[RTB]display ip routing-table
Destination/Mask Proto Pre Cost NextHop Interface
2.0.0.0/8 ISIS 15 84 12.12.12.1 Serial0

## Slide 37
Solution 1: Filter Routes
Lo0:2.2.2.2
RIP
ISIS
RTA
RTD
RTC
RTB
24.24.24.2
isis 1
import-route rip 1
display ip routing-table
Destination/Mask Proto Pre Cost NextHop Interface
2.0.0.0/8 RIP 100 1 24.24.24.2 Serial1
acl 2001
rule 5 deny source 2.0.0.0 0.255.255.255
rule 10 permit
isis 1
filter-policy 2001 import

## Slide 38
Solution 2: Adjust Protocol Priorities
Lo0:2.2.2.2
RTA
RTD
RTC
RTB
24.24.24.2
RIP
ISIS
isis 1
preference 150
display ip routing-table
Destination/Mask Proto Pre Cost NextHop Interface
2.0.0.0/8 RIP 100 1 24.24.24.2 Serial1
isis 1
import-route rip 1

## Slide 39
Other Problems Caused by Multi-Protocol - Loop
Lo0:2.2.2.2/32
ISIS
OSPF
RTA
RTB
RTC
RTD
RTE
①import direct cost 2
②Dest. ASE 150 2
③Dest. ASE 150
④import ospf
⑤Dest. ISIS 15
⑥Dest. ISIS 15
③Dest. ASE 150
⑦import isis
⑧Dest. ASE 150 1

## Slide 40: Other Problems Caused by Multi-Protocol - Loop
Lo0:2.2.2.2/32
ISIS
OSPF
RTA
RTB
RTC
RTD
RTE
import direct cost 2
Dest. ASE 150 2
Dest. ASE 150
import ospf
Dest. ISIS 15
Dest. ISIS 15
Dest. ASE 150
import isis
Dest. ASE 150 1

## Slide 41
Solution 1: Filter Routes
Lo0:2.2.2.2/32
ISIS
OSPF
RTA
RTB
RTC
RTD
RTE
acl 2001
rule 0 deny source 2.0.0.0 0.255.255.255
rule 1 permit
ospf 1
import-route isis 1 route-policy RP1
route-policy RP1 permit node 10
if-match acl 2001
isis 1
import-route ospf 1
ospf 1
import-route direct cost 2

## Slide 42
Solution 2: Adjust Protocol Priorities
Lo0:2.2.2.2/32
ISIS
OSPF
RTA
RTB
RTC
RTD
RTE
12.12.12.1
isis 1
preference 160
ospf 1
import-route isis 1
isis 1
import-route ospf 1
ospf 1
import-route direct cost 2
display ip routing-table
Destination/Mask Proto Pre Cost NextHop Interface
2.2.2.2/32 O_ASE 150 2 12.12.12.1 Serial0

## Slide 43
Can the IP prefix list be used to filter IP packets?
Which methods can be used to adjust traffic paths?
What problems may be caused by route importing and what are the solutions?
Notes: Answer: The IP prefix list can filter only routing information, but cannot filter IP packets.
Answer: Routing policy and policy-based routing.
Answer: The problems such as sub-optimal path and route loop may occur. The solutions include route filtering and priority adjustment.