## Slide 1: IS-IS Principles and Configurations

## Slide 2
Intermediate System-to-Intermediate System (IS-IS) is a link-state based IGP. It uses the Shortest Path First (SPF) algorithm to calculate routes. IS-IS is a dynamic routing protocol initially designed by the International Organization for Standardization (ISO) for its Connectionless Network Protocol (CLNP).
To support IP routing, the Internet Engineering Task Force (IETF) extends and modifies IS-IS in RFC 1195. This enables IS-IS to be applied to TCP/IP and OSI environments. This type of IS-IS is called Integrated IS-IS. IS-IS has been widely used in large ISP networks because of its simplicity and high scalability.

## Slide 3
Upon completion of this section, you will be able to:
  Master IS-IS principles and configurations
  Be familiar with differences between IS-IS and OSPF

## Slide 4
IS-IS Principles
Differences Between IS-IS and OSPF
IS-IS Configurations

## Slide 5
Backbone network:
Flat area, fast convergence, and high transmission volume
Campus network:
A variety of areas, changeable policies, and fine-grained scheduling
Application
ER
CS
SW
ER
CS
SW
SW
OSPF
CE
PE
CE
PE
PE
PE
PE
CE
CE
IS-IS+BGP
Notes: Campus network characteristics:
  It is an application-oriented network, which is intended for enterprise network users.
  The number of routers is relatively small, the dynamic routing LSDB capacity is relatively low, and the number of Layer 3 routing domains is relatively small.
  Compared with a backbone network, a campus network has a smaller coverage area and sufficient bandwidth. The link state protocol occupies less bandwidth.
  Routing policies and policy-based routing (PBR) are changed frequently, so fine-grained routing is required.
  There are a variety of OSPF route types (internal and external routes), area types (backbone, common, and special areas), and network types (a maximum of five network types), as well as well-designed cost calculation (configured based on bandwidth).
Backbone network characteristics:
  It is a service-oriented network and built by Internet Service Providers (ISPs) to provide Internet services to terminal users.
  There are a large number of routers. Therefore, route scheduling is critical.

## Slide 6
Notes: The architecture is flat, requiring IGP as basic routing protocols to serve BGP.
The LSDB is large and sensitive to link convergence and the link cost is high.
Simplicity, high efficiency, and high scalability are required to meet various customer service requirements (IPv6/IPX).
IS-IS has many advantages in backbone networks, including IS-IS fast algorithm (enhanced PRC), simple packet structure (TLV), fast neighbor relationship establishment, and large-capacity route transmission.

## Slide 7
Origin
Application
layer
Presentation
layer
Session
layer
Transport
layer
Network
layer
Data link
layer
Physical
layer
OSI
Application
layer
Transport
layer
Network
layer
Data link
layer
Physical
layer
TCP/IP
ARP
TCP
IP
ES-IS
TP0-TP4
CLNP
IS-IS
OSPF
Integrated
IS-IS
Integrated IS-IS characteristics:
  Supports CLNP and IP networks.
  Works at the data link layer.
OSPF characteristics:
  Supports only IP networks.
  Works at the IP layer.
Notes: IS-IS is a dynamic routing protocol initially designed by the International Organization for Standardization (ISO) for its Connectionless Network Protocol (CLNP).
To support IP routing, the Internet Engineering Task Force (IETF) extends and modifies IS-IS in RFC 1195. This enables IS-IS to be applied to TCP/IP and OSI environments. This type of IS-IS is called Integrated IS-IS. Unless otherwise stated, IS-IS refers to Integrated IS-IS.
IS-IS is an Interior Gateway Protocol (IGP) and used within an Autonomous System (AS). IS-IS is a link state protocol and uses Shortest Path First (SPF) algorithm to calculate routes.

## Slide 8
Establish a neighbor relationship
Route Calculation
Perform SPF route calculation
Shortest path tree
This process is
similar to that in OSPF
Hello
Synchronize the LSDB
LSDB
LSP1
LSP2
-------
LSDB
LSP3
LSP4
-------
Notes: Neighbor relationship establishment:
  Before establishing a neighbor relationship, devices on two ends exchange Hello packets and negotiate parameters, including the circuit type (level-1/level-2), hold time, network type, supported protocol, area ID, system ID, PDU length, and interface IP address.
Link information exchange:
  Different from OSPF, IS-IS exchanges link state information using link state PDUs (LSPs) instead of link state advertisements (LSAs). In IS-IS, CSNPs and PSNPs are used to synchronize the LSDB and request as well as acknowledge link state information (link state information summary). Detailed topology of link state information and routing information are transmitted using LSPs.
Route calculation:
  IS-IS SPF calculation is similar to OSPF SPF calculation except that the IS-IS algorithm separates the topology and IP network segment and speeds up network convergence.

## Slide 9
Address Structure
High Order DSP
System ID
SEL
IDI
AFI
Area ID (1-13B)
6B
1B
NSAP
IDP
DSP
49.0001. 0000.0000.0001.00
Area ID System ID N-SEL
  NET is a special type of NSAP address (SEL=00). When configuring IS-IS on a router, you only need to consider the NET. For example:
TCP/IP protocol stack | IP protocol | IP address | OSPF | Area ID+Router ID
OSI | CLNP protocol | NSAP address | IS-IS | NET identifier
Notes: NSAP address:
  The IDP is equal to the network number in an IP address. As defined by the ISO, the IDP consists of the Authority and Format Identifier (AFI) and Initial Domain Identifier (IDI). The AFI specifies the address allocation authority and address format; the IDI identifies a domain.
  The DSP is equal to the subnet number and host number in an IP address. The DSP consists of the High Order DSP (HODSP), system ID, and NSAP Selector (SEL). The HODSP is used to divide areas; the system ID identifies a host; the SEL indicates the service type.
  The IDP together with the HODSP of the DSP can identify a routing domain and the areas in a routing domain; therefore, the combination of the IDP and HODSP is referred to as an area address, which is equal to an area ID in OSPF.
  System ID uniquely identifies a host or router in an area and has a fixed length of 48 bits (6 bytes).
  The role of an SEL is similar to the Protocol field of an IP header. Different network layer services match different SELs. The SEL is always 00 in IP.

## Slide 10
Notes: NET:
An NET indicates the network layer information of an IS itself and can be regarded as a special type of NSAP (SEL=0). The NET length is the same as the NSAP length. The maximum NSAP length is 20 bytes and its minimum length is 8 bytes. When configuring IS-IS on a router, you can configure only a NET instead of an NSAP.
An IS-IS process can be configured with a maximum of three NETs. When configuring multiple NETs, ensure that their system IDs are the same.

## Slide 11
IS-IS routers are classified into three types:
  Level-1 router: supports only Level-1 LSDB.
  Level-2 router: supports only Level-2 LSDB.
  Level-1-2 router: is the default router type and supports both Level-1 and Level-2 LSDBs.
Router Types
To establish a Level-1 adjacency, ensure that two routers use the same area ID.
Same area
Area 49.0001
Different areas
Area 49.0001
Area 49.0002
×
Notes: Level-1 router:
  A Level-1 router establishes neighbor relationships with only Level-1 and Level-1-2 routers in the same area. It maintains a Level-1 LSDB, which contains intra-area routing information and forwards packets destined for other areas to the nearest Level-1-2 router. A Level-1 router can establish only Level-1 adjacencies.
Level-2 router:
  A Level-2 router manages inter-area routing. It can establish neighbor relationships with Level-2 routers in the same or different areas and with Level-1-2 routers in different areas. It maintains a Level-2 LSDB, which contains inter-area routing information. A Level-2 router can establish only Level-2 adjacencies.
Level-1-2 router:
  A router, which belongs to both Level-1 area and Level-2 area, is called a Level-1-2 router. A Level-1-2 router maintains two LSDBs, that is, a Level-1 LSDB and a Level-2 LSDB. The Level-1 LSDB is used for intra-area routing and the Level-2 LSDB is used for inter-area routing.

## Slide 12
Notes: A Level-1-2 router can establish Level-1 neighbor relationships with Level-1 routers in the same area. It can also establish Level-2 neighbor relationships with Level-2 routers and Level-1-2 routers in other areas.
IS-IS routers in different areas can only establish Level-2 adjacencies:
A Level-2 router can establish an adjacency with other Level-2 routers.
A Level-1-2 router can establish an adjacency with other Level-2 routers.
A Level-1-2 router can establish an adjacency with other Level-1-2 routers.

## Slide 13
IS-IS currently supports only P2P and broadcast network types.
Hello Packet
Broadcast multiple access network type
P2P
Broadcast
Point-to-Point IIH
L1 LAN IIH
Mac:0180-c200-0014
L2 LAN IIH
Mac:0180-c200-0015
OR
Point-to-point network type
Notes: Hello protocol data unit (Hello PDU):
  Hello packets are used to discover neighbors, negotiate parameters, maintain neighbor relationships, and function as Keepalive packets.
  Like OSPF, IS-IS establishes neighbor relationships by exchanging Hello packets. Hello packets are classified into three types based on scenarios.
  In a broadcast network, Level-1 IS-IS routers use Level-1 LAN IS-IS Hello (IIH) packets with the destination multicast MAC address 0180-c200-0014.
  In a broadcast network, Level-2 IS-IS routers use Level-2 LAN IIH packets with the destination multicast MAC address 0180-c200-0015.
  P2P IIH packets are used in a non-broadcast network and do not carry any field indicating the DIS (also called pseudo node). IIH packets need to use the padding field for negotiating the size of packets sent between devices on the two ends.
IS-IS supports the following network types:
  P2P network type.
  Broadcast multiple access network type.
  In special environments such as frame relay, sub-interfaces can be created to support the P2P network type.

## Slide 14
Neighbor Relationship Establishment
ISO10589 defines two-way handshake, while RFC3373 defines P2P three-way handshake.
point-to-point IIH
RTA
RTB
SYS ID 0000.0000.0001
SYS ID 0000.0000.0002
point-to-point IIH
State: up
State: up
Two-way handshake
Establishing neighbor relationship of the multicast access (MA) network type requires three-way handshake.
RTA
RTB
SYS ID 0000.0000.0001
SYS ID 0000.0000.0002
LAN IIH (system ID: 0000.0000.0001 neighbor: null)
LAN IIH (system ID: 0000.0000.0002 neighbor: RTA)
LAN IIH (system ID: 0000.0000.0001 neighbor: RTB)
State: initialized
State: up
State: up
Three-way handshake
DIS election
Notes: On a P2P link, a neighbor relationship can be established through two-way handshake and three-way handshake.
  In two-way handshake, upon receiving a Hello packet from its neighbor, a router considers the neighbor Up and establishes a neighbor relationship with the neighbor. However, there is a risk of unidirectional communication.
  In three-way handshake, a neighbor relationship is established after P2P IIHs are sent three times, similar to neighbor relationship establishment on a broadcast link.
On a broadcast link, a neighbor relationship is established using LAN IIH packets through three-way handshake.
  When a router receives from its neighbor a Hello PDU that does not contain its system ID, the state machine enters the initialized state.
  The state machine enters the Up state only when the router receives from its neighbor a Hello PDU that contains its system ID, eliminating the risk of unidirectional communication.
  On a broadcast network, the DIS (also called pseudo node) will be elected after the neighbor state becomes Up. The DIS functions similarly to the Designated Router (DR) in OSPF.

## Slide 15
Comparisons Between DIS and DR
Virtual router
(pseudo node)
Leve-1
Leve-1
Leve-1-2
DIS
Item | IS-IS DIS | OSPF DR
Election priority | Devices with all priorities participate in DIS election | The device with priority 0 does not participate in DR election
Election waiting time | Two Hello intervals | 40s
Backup | No backup | BDR for backup
Adjacency | All routers establish adjacencies | DR others establish 2-way neighbor relationships
Preemption | Yes | No
Function | Send CSNPs periodically to guarantee LSDB synchronization on MA networks. | Reduce LSA flooding
Leve-1
Leve-1-2
Leve-1
Notes: DIS and pseudo node:
  DIS is short for the Designated IS.
  Pseudo node is a virtual router created by the DIS in a broadcast network.
DIS characteristics:
  The DIS needs to be elected on a broadcast network. After a neighbor relationship is established, a router participates in DIS election after waiting for two Hello intervals. A Hello packet contains the Priority field. The device with the largest priority value is elected as the DIS of the broadcast network. If the devices have the same priority, the device with the largest interface MAC address is elected as the DIS. In IS-IS, the interval at which the DIS sends Hello packets defaults to 10/3 seconds, while the interval at which non-DIS routers send Hello packets is 10s.
Comparisons between DIS and DR:
  In IS-IS, the router with priority 0 also takes part in DIS election. In OSPF, the router with priority 0 does not take part in DR election.
  In OSPF, DR/BDR election requires 40s waiting time and is complicated. In IS-IS, DIS election requires two Hello intervals and is simple and fast.

## Slide 16
Notes: In IS-IS, only the DIS is elected. In OSPF, both the DR and BDR are elected, and BDR functions as the backup of the DR.
After election is complete, if a new router with a higher priority is added, it can become the new DIS in IS-IS but cannot become the new DR in OSPF.
After election is complete, all routers on an IS-IS network establish adjacencies. In OSPF, DR others establish only full adjacency relationships with the DR/BDR. DR others establish only 2-way neighbor relationships with each other.
DIS and DR functions:
Both the DIS and DR function as a virtual node during SPF calculation, simplifying MA network topology.
Both the DIS and DR are designed to reduce flooding of LSPs/LSAs.
In IS-IS, the DIS sends CSNPs to synchronize the LSDB (IS-IS extension).

## Slide 17
TLV
IS-IS packet structure
TYPE
LENGTH
VALUE
  LSP PDU: is used to exchange link state information.
  Real node LSP
  Pseudo node LSP (exists only in broadcast links)
  SNP PDU: is used to maintain and synchronize the LSDB and carries summary information.
  CSNP (used to synchronize LSPs)
  PSNP (used to request and acknowledge LSPs)
Link State Information Transmission
IS-IS packets fall into two types: Level-1 and Level-2 packets. The destination MAC addresses of all IS-IS packets in MA networks are multicast MAC addresses:
Level-1 address: 0180-C200-0014
Level-2 address: 0180-C200-0015
Notes: IS-IS TLV:
  TLV indicates the type, length, and value. It is a data structure and contains three fields.
  Using TLV to construct packets can ensure flexibility, scalability, and stable packet structure. If new characteristics are added, only new TLVs need to be added, removing the need to change the packet structure.
  Using TLV to indicate network topology and routing information can improve packet flexibility and scalability.
Link State Protocol PDU (LSP PDU):
  LSPs are similar to LSAs in OSPF and used to transmit link state information, including the topology and network ID.
  Level-1 LSPs are transmitted by Level-1 routers.
  Level-2 LSPs are transmitted by Level-2 routers.
  Level-1-2 routers can transmit both Level-1 and Level-2 LSPs.
  LSPs contain two important fields: ATT field and IS-Type field. The ATT field indicates that an LSP is transmitted by a Level-1-2 router. The IS-Type field indicates whether an LSP is generated by a Level-1 or Level-2 router.

## Slide 18
Notes: The LSP update interval is 15 minutes and the LSP aging time is 20 minutes. The aging of an LSP requires the waiting time of 20 minutes and the delay of 60 seconds. The LSP retransmission time is 5 seconds.
Sequence Number PDU (SNP PDU):
Complete Sequence Number PDU (CSNP) contains the summary of all LSPs in an LSDB and can be used to ensure LSDB synchronization between neighboring routers.
Partial Sequence Number PDU (PSNP) contains the summary of some LSPs in an LSDB and can be used to request and acknowledge LSPs.
CSNPs are similar to DD packets in OSPF and used to transmit the summary of all link information in an LSDB. PSNPs are similar to LSR or LSAck packets in OSPF and used to request and acknowledge some link information.

## Slide 19
Link State Information Exchange
CSNP
A.00-00
PSNP
A.00-00
LSP
A.00-00

PSNP
A.00-00
Retransmission expires
LSP
A.00-00
PSNP
A.00-00
Retransmit PSNP
  CSNPs are sent only once on a P2P network. That is, a CSNP is sent immediately after a neighbor relationship is established.
PSNP
A.00-00
B.00-00
B.01-00
LSP
C.00-00
C.00-01
CSNP
A.00-00
B.00-00
B.01-00
C.00-00
C.00-01
LSP
A.00-00
B.00-00
B.01-00
  CSNPs are multicast only by the DIS on an MA network at the default interval of 10s.
Pseudo node LSP
Fragment LSP
RTA
RTB
P2P
RTA
RTC
RTB DIS
MA
Notes: LSDB synchronization on a P2P network:
  After establishing a neighbor relationship, RTA and RTB send a CSNP to each other. If the LSDB of the neighbor and the received CSNP are not synchronized, the neighbor sends a PSNP to request the required LSP.
  If RTA does not receive any PSNP from RTB after the LSP retransmission timer expires, RTA retransmits the required LSP until it receives a PSNP from RTB.
LSDB synchronization between the newly added router and DIS on an MA network:
  Assume that the newly added router RTC has established neighbor relationships with RTB (DIS) and RTA.
  After establishing neighbor relationships, RTC sends its LSP to the multicast address (01-80-C2-00-00-14 in a Level-1 area and 01-80-C2-00-00-15 in a Level-2 area). Then all neighbors on the network receive this LSP.
  The DIS on the network adds the LSP received from RTC to its LSDB, waits for the expiry of the CSNP timer (the DIS sends CSNPs at an interval of 10s). After the CSNP timer expires, the DIS sends a CSNP to synchronize the LSDBs on the network.
  RTC receives the CSNP from the DIS, checks its LSDB, and then sends a PSNP to the DIS to request the LSPs that it does not have. For example, RTC does not have the LSPs of RTA and RTB.
  RTB (the DIS) receives the PSNP and then sends the LSPs required by RTC for LSDB synchronization.

## Slide 20
Routing Algorithms
RTA
RTE
RTA
RTB
RTC
RTD
RTE
100Mbps
2Mbps
100Mbps
100Mbps
IS-IS route cost calculation:
  The default interface cost is 10.
SPF calculation process:
  Complete LSDB synchronization within a single area.
  Generate the network topology.
  Generate the shortest path tree, using the local node as the root.
Notes: IS-IS route calculation characteristics:
  A router in an area performs the full SPF algorithm when it starts for the first time.
  If the received LSPs are updated and part of the topology is changed, the router performs incremental SPF (ISPF) algorithm.
  If only routing information is changed, the router performs partial route calculation (PRC).
  Because the algorithm that separates the topology and network is used, the route convergence speed is improved.
IS-IS interface cost calculation:
  Narrow mode: The default interface cost is 10, and the manually configured interface cost ranges from 1 to 63.
  Wide mode: The default interface cost is 10, and the manually configured interface cost ranges from 1 to 16777215.
  If the auto-cost enable command is executed in an IS-IS process, the interface cost is calculated based on the interface bandwidth in both narrow mode and wide mode, and only the reference rules vary slightly in the two modes.

## Slide 21
The IS-IS area boundary is a router, while the OSPF area boundary is a router interface.
Network Hierarchy and Routing Domain
L2
L2
L2
L1/2
L2
L1/2
L1
L1/2
L1
L1
L1
L1/2
L1
L1
Area 49.0001
Area 49.0002
Area 49.0003
Area 49.0004
Area 49.0005
Backbone
Notes: IS-IS topology:
  IS-IS uses a two-level hierarchy (backbone area and non-backbone area) to support large-scale routing networks. Generally, Level-1 routers are deployed in non-backbone areas, whereas Level-2 and Level-1-2 routers are deployed in the backbone area. Each non-backbone area connects to the backbone area through Level-1-2 routers.
  The figure shows a network that runs IS-IS. The network is similar to an OSPF network typology with multiple areas. The backbone area contains all Level-2 routers and Level-1-2 routers.
  Level-1-2 routers can belong to different areas. In Level-1 area, Level-1-2 routers maintain a Level-1 LSDB. In Level-2 area, Level-1-2 routers maintain a Level-2 LSDB.
As shown in the preceding figure, differences between IS-IS and OSPF are as follows:
  In IS-IS, each link can belong to different areas. In OSPF, each link belongs to only one area.
  In IS-IS, no area is defined as the backbone area. In OSPF, Area 0 is defined as the backbone area.
  In IS-IS, Level-1 and Level-2 routers use the SPF algorithm to generate their shortest path trees. In OSPF, the SPF algorithm is used only in the same area, and inter-area routes need to be forwarded through the backbone area.

## Slide 22
L1
L1
Maintain L1 LSDB
L1/2
L1 neighbor
Area 49.0001
L1 neighbor
Backbone area
Maintain L2 LSDB
L2
Area 49.0002
L2 neighbor
L2 neighbor
L2
Area 49.0001 accesses Area 49.0002
  The Level-1-2 router RTA generates an LSP with the ATT bit set to 1.
  A Level-1 router generates a default route with the next hop pointing to the Level-1-2 router after receiving the LSP with the ATT bit 1.
Area 49.0002 accesses Area 49.0001
  The Level-1-2 router, RTA, adds specific routes to Area 49.0001 in the Level-2 LSDB.
  A Level-2 router calculates specific routes to Area 49.0001 through SPF calculation.
RTA
Inter-Area Routing
Notes: Level-1 router characteristics:
  It has only a Level-1 LSDB. Its LSDB has only LSPs of routers in the local area.
  Its routing table does not contain routing information of other areas.
  Its routing table has one default route with the next hop pointing to a Level-1-2 router.
Level-2 router characteristics:
  It has only a Level-2 LSDB. Its LSDB has LSPs of routers in the backbone area but no LSPs of Level-1 routers.
  Its routing table contains routing information of the entire network.
Level-1-2 router characteristics:
  It has both Level-1 and Level-2 LSDBs. The Level-1 LSDB has LSPs of routers in the local area, and the Level-2 LSDB has LSPs of routers in the backbone area.
  It sets the ATT bit to 1 in its generated Level-1 LSP.
  Its routing table contains routing information of the entire network.

## Slide 23
IS-IS Principles
Differences Between IS-IS and OSPF
IS-IS Configurations

## Slide 24
Differences Between IS-IS and OSPF
Use IS-IS or OSPF based on your service requirements
Item | IS-IS | OSPF
Network types | Less | More
Cost style | Complicated | Simple
Area types | Less | More
Packet types | Simple | Various
Route convergence | Faster | Fast
Scalability | High | Medium
Routing load capacity | Higher | High
Notes: Network types and cost style:
  IS-IS supports only two network types and defines the same default cost for all bandwidths. OSPF supports four network types and defines the cost based on bandwidth.
Area types:
  IS-IS areas are classified into Level-1 and Level-2 areas. Level-2 area is the backbone area and has all specific routes. There are only default routes from Level-1 to Level-2 areas. OSPF areas are classified into the backbone area, common area, and special area. Devices in common and special areas must communicate across the backbone area.
Packet types:
  IS-IS uses only LSPs to transmit routing information and does not differentiate internal and external routing information, so IS-IS is simple and efficient. OSPF uses a variety of LSAs to transmit routing information, including Types 1, 2, 3, 4, 5, and 7, and applies to fine-grained scheduling and calculation.

## Slide 25
Notes: Routing algorithm:
In IS-IS, when changes occur on the network segment where a node in an area resides, PRC algorithm is triggered, ensuring fast route convergence and low route calculation cost. In OSPF, network address is used for building the network topology, and ISPF algorithm is triggered when the network segment address in an area is changed, which is complicated.
Scalability:
In IS-IS, all routing information is transmitted using TLVs, ensuring simple structure and providing easy scalability. For example, to support IPv6, only two TLVs are added to IS-IS. Additionally, IS-IS also supports protocols such as IPX. OSPF is developed to support IP and provides two independent versions OSPFv2 and OSPFv3 to support IPv4 and IPv6.

## Slide 26
Terms
Abbreviation | OSI Term | IETF Term
IS | Intermediate System | Router
ES | End System | Host
DIS | Designated Intermediate System | Designated Router in OSPF
SysID | System ID | Router ID in OSPF
LSP | Link State PDU | LSA in OSPF
IIH | IS-IS Hello PDU | Hello packet in OSPF
PSNP | Partial Sequence Number PDU | LSR or LSAck in OSPF
CSNP | Complete Sequence Number PDU | DD packet in OSPF

## Slide 27
IS-IS Principles
Differences Between IS-IS and OSPF
IS-IS Configurations

## Slide 28
In the figure, all routers in the customer network need to run IS-IS to ensure reachable routes on the network. All IS-IS processes use the process ID 100. RTA is the DIS in Area 49.0001. The network between RTD and RTE must be P2P network. RTE imports the direct route 192.168.X.X and requires RTA to access Area 49.0002 through the optimal path.
Perform the configuration correctly to meet the preceding customer requirements.
IS-IS Route Configuration Requirements
import1
RTB
RTC
RTD
Area 49.0001
Area 49.0002
Level-1
Level-2
RTA
192.168.1.0/24;
192.168.2.0/24;
192.168.3.0/24;
G0/0/0
G0/0/0
G0/0/1
G0/0/1
G0/0/0
G0/0/0
G0/0/0
S1/0/0
S1/0/0
100Mbps
2Mbps
RTE
Notes: NET address number:
  RTA: 49.0001.0000.0000.0001:00
  RTB: 49.0001.0000.0000.0002:00
  RTC: 49.0001.0000.0000.0003:00
  RTD: 49.0001.0000.0000.0004:00
  RTE: 49.0001.0000.0000.0005:00

## Slide 29
IS-IS Route Configuration (1)
isis 100
network-entity 49.0001.0000.0000.0001.00
is-level level-1
#
interface GigabitEthernet0/0/0
isis enable 100
isis dis-priority 120 level-1
isis 100
network-entity 49.0001.0000.0000.0002.00
#
interface GigabitEthernet0/0/0
isis enable 100
isis 100
network-entity 49.0001.0000.0000.0003.00
#
interface GigabitEthernet0/0/0
isis enable 100
import1
RTB
RTC
RTD
Area 49.0001
Area 49.0002
Level-1
Level-2
RTA
192.168.1.0/24;
192.168.2.0/24;
192.168.3.0/24;
G0/0/0
G0/0/0
G0/0/1
G0/0/1
G0/0/0
G0/0/0
G0/0/0
S1/0/0
S1/0/0
100Mbps
2Mbps
RTE
Notes: Intra-area routing configuration roadmap:
  Service configuration of Area 49.0001:
    Configure a NET for each router in IS-IS process 100.
    Configure RTA as a Level-1 router in IS-IS process 100 and retain the default IS-IS level of RTB and RTC as Level-1-2 routers.
    Enable IS-IS on interfaces of RTA, RTB, and RTC.
    Change the DIS priority of RTA to be the highest priority so that RTA becomes the DIS.

## Slide 30
IS-IS Route Configuration (2)
import1
RTB
RTC
RTD
Area 49.0001
Area 49.0002
Level-1
Level-2
RTA
192.168.1.0/24;
192.168.2.0/24;
192.168.3.0/24;
G0/0/0
G0/0/0
G0/0/1
G0/0/1
G0/0/0
G0/0/0
G0/0/0
S1/0/0
S1/0/0
100Mbps
2Mbps
RTE
isis 100
network-entity 49.0002.0000.0000.0005.00
is-level level-2
#
interface GigabitEthernet0/0/0
isis enable 100
isis circuit-type P2P
isis 100
network-entity 49.0002.0000.0000.0004.00
is-level level-2
#
interface GigabitEthernet0/0/0
isis enable 100
isis circuit-type P2P
Notes: Intra-area routing configuration roadmap:
  Service configuration of Area 49.0002:
    Configure a NET for each router in IS-IS process 100.
    Configure RTD and RTE as Level-2 routers in IS-IS process 100.
    Enable IS-IS on interfaces of RTD and RTE.
    Change the network type of interfaces on RTD and RTE as P2P.

## Slide 31
IS-IS Route Configuration (3)
import1
RTB
RTC
RTD
Area 49.0001
Area 49.0002
Level-1
Level-2
RTA
192.168.1.0/24;
192.168.2.0/24;
192.168.3.0/24;
G0/0/0
G0/0/0
G0/0/1
G0/0/1
G0/0/0
G0/0/0
G0/0/0
S1/0/0
S1/0/0
100Mbps
2Mbps
RTE
isis 100
network-entity 49.0001.0000.0000.0002.00
import-route isis level-2 into level-1
#
interface GigabitEthernet0/0/1
isis enable 100
isis 100
network-entity 49.0001.0000.0000.0003.00
import-route isis level-2 into level-1
#
interface Serial 1/0/0
isis enable 100
isis 100
import-route direct
Notes: Inter-area routing configuration roadmap:
  Configure RTB as a Level-1-2 router and configure a NET for RTC in IS-IS process 100.
  Enable IS-IS on interfaces.
  Import the direct route on RTE.
Route leaking:
  If a Level-1 area has more than two Level-1-2 routers, a Level-1 router in the Level-1 area accesses other areas through the nearest Level-1-2 router, but only the intra-area cost is calculated. If the cost from the nearest Level-1-2 router in a Level-2 area to the destination network is high, the sub-optimal path exists. In this situation, route leaking needs to be performed to import specific routes (including the cost) of the Level-2 area into the Level-1 area, and then the Level-1 router calculates the optimal path to access other areas. This example requires RTA to access Area 49.0002 through the optimal path. Because the bandwidth of the link connecting RTB to RTD is relatively high, it is better to transmit traffic through RTB. To do this, in the IS-IS processes of RTB and RTC, import Level-2 routes into the Level-1 area. The LSDB of RTA contains all specific routes of the Level-2 area so that RTA can select the optimal path to reach Area 49.0002.

## Slide 32
How many IS-IS router types exist?
What is the function of PSNPs in neighbor interaction?
What are the advantages of IS-IS compared with OSPF?
Notes: Answer: IS-IS routers are classified into Level-1 router, Level-2 router, and Level-1-2 router.
Answer: PSNPs are used to request and acknowledge LSPs.
Answer: IS-IS has simple packet structure, strong route transmission capacity, well-designed routing algorithm, and high scalability.